## Slide 1: Net-Zero House Study
Engineering 333 Class Project
Senior Mechanical Engineering Students
12/02/2014

## Slide 2: What would it take to make a home in Grand Rapids Net-Zero?
Background | Assess | Reduce | Generate | Offset | Results

## Slide 3: What is Net-Zero?
Background | Assess | Reduce | Generate | Offset | Results
https://www.efficiencyvermont.com/sf-images/default-source/bbd/residential_ netzero_graphic_final_cs5_largetext-01DAC6DAB02C1A.png?sfvrsn=2
Notes: A Net-Zero Home produces as much energy as it consumes in a calendar year

## Slide 4
Background | Assess | Reduce | Generate | Offset | Results
Figure 1. Historical US Energy Consumption Percentage by Sector.
http://www.eia.gov/totalenergy/data/annual/showtext.cfm?t=ptb0201a
Chart: 
Historical US Energy Consumption Percentage by Sector

## Slide 5: Why investigate this?
Background | Assess | Reduce | Generate | Offset | Results
God spoke: “Let us make human beings in our image, make them reflecting our nature so they can be responsible for the fish in the sea, the birds in the air, the cattle, and yes, Earth itself, and every animal that moves on the face of Earth.”
- Genesis 1:26

## Slide 6
Background | Assess | Reduce | Generate | Offset | Results
Koetje
Evenhouse
DeMaagd
Heffner
Cooper
Affholter
Newhof
Boer

## Slide 7
Background | Assess | Reduce | Generate | Offset | Results
Reeds Lake
1,250 ft2
2,000 ft2
3,000 ft2
4,000 ft2
Affholter
Boer
Cooper
DeMaagd
Evenhouse
Heffner
Koetje
Newhof
Calvin College
E Beltline

## Slide 8: Net-Zero Implementation Process
Background | Assess | Reduce | Generate | Offset | Results
Assess
Generate
Offset
Reduce

## Slide 9
Background | Assess | Reduce | Generate | Offset | Results
High Energy Consumption
Low Energy Consumption
$5
$10

## Slide 10
Background | Assess | Reduce | Generate | Offset | Results
Assess: Energy Audits
Affholter
Percentage of Total Electricity Usage
Notes: Energy Audits are the prologue to net zero. They map out where a house is and they point towards feasible options for a house.
An energy audit is a walkthrough of the house that catalogs what every energy user is, and how much energy they use.
Transition #1.
Here, we see the audit results of the Affholter House.
Appliances take up a ton of energy
Most appliances are in the kitchen
Lighting is a significant factor in energy usage
Entertainment energy spending is minimal, so lifestyle changes may not be a high-value option.

## Slide 11
Background | Assess | Reduce | Generate | Offset | Results

## Slide 12: Energy Reduction
Background | Assess | Reduce | Generate | Offset | Results
http://s.hswstatic.com/gif/led-light-bulb-1.jpg
http://dakselfstorage.com/wp-content/uploads/2014/10/kicthen-appliance-storage.jpg
http://nesbuildingsolutions.com/wp-content/uploads/2013/01/spray-foam-wall-insulation-1.gif
http://compass.xbox.com/assets/3a/17/3a17ef9b-e017-4282-9f25-6b7e35b0c27a.jpg?n=ui-xbox-360-cle-video-xbox-video-1000x487.jpg
Lighting
Appliances
Insulation
Lifestyle Changes

## Slide 13: LED Lighting – Cooper House
Background | Assess | Reduce | Generate | Offset | Results
Cooper
http://www.marco.org/media/2013/09/cree-led-flaw.jpg
http://assets.inhabitat.com/wp-content/blogs.dir/1/files/2011/08/Zimbabwe-CLF-bulb-exchange-3-537x402.jpg
Notes: 5826.6 kW-hr / year​
$700 / year

## Slide 14
Background | Assess | Reduce | Generate | Offset | Results

## Slide 15
Background | Assess | Reduce | Generate | Offset | Results
$957.5

## Slide 16
Background | Assess | Reduce | Generate | Offset | Results
$957.5
$400
$48
$195
$1,395

## Slide 17: Appliances – DeMaagd House
Background | Assess | Reduce | Generate | Offset | Results
http://www.homeenergytune-ups.com/wp-content/uploads/2013/11/energyefficient.jpg
DeMaagd
Notes: 450 kW-hr / year​
$54 / year

## Slide 18
Background | Assess | Reduce | Generate | Offset | Results

## Slide 19
Background | Assess | Reduce | Generate | Offset | Results
$1,400

## Slide 20
Background | Assess | Reduce | Generate | Offset | Results
$7,100
$4,128
$2,634
$1,520
$2,710
$2,000

## Slide 21: Insulation – Koetje House
Background | Assess | Reduce | Generate | Offset | Results
http://iandsinsulation.com/images/TomSpraying.jpg
Koetje
Notes: Previously no wall insulation
361 therms/ year​savings
$380 / year savings

## Slide 22
Background | Assess | Reduce | Generate | Offset | Results

## Slide 23
Background | Assess | Reduce | Generate | Offset | Results
$750

## Slide 24
Background | Assess | Reduce | Generate | Offset | Results
$750
$1,730
$10,700
$610

## Slide 25: Lifestyle Changes - Boer House
Background | Assess | Reduce | Generate | Offset | Results
http://www.bose.com.hk/upload/products/videowave/videowave_bl_lg.jpg
Boer
Notes: 265 kW-hr / year​
$30 / year

## Slide 26
Background | Assess | Reduce | Generate | Offset | Results

## Slide 27
$0
Background | Assess | Reduce | Generate | Offset | Results

## Slide 28
Background | Assess | Reduce | Generate | Offset | Results
$0
$0
http://www.arcticspas.com/

## Slide 29
Background | Assess | Reduce | Generate | Offset | Results

## Slide 30: Energy Generation
Background | Assess | Reduce | Generate | Offset | Results
http://www.theecoambassador.com/Geothermalenergy.html
http://www.nerg.co.uk/NerG/biomass-heating/
http://www.makeitsolar.com/solar-energy-information/02-solar-energy.htm
http://commons.wikimedia.org/wiki/File:Solar_panels_on_a_roof.jpg
http://www.triplepundit.com/2014/01/wind-energy-industry-receive-tax-credits/

## Slide 31: Geothermal - Affholter House
Background | Assess | Reduce | Generate | Offset | Results
http://www.esipowercorp.com/Portals/139609/images/Vertical_Loop.jpg
Affholter
Notes: Space Confinement issues
Horizontal Loop is inexpensive if home has the space

## Slide 32
Background | Assess | Reduce | Generate | Offset | Results

## Slide 33
Background | Assess | Reduce | Generate | Offset | Results
$18,200

## Slide 34
Background | Assess | Reduce | Generate | Offset | Results
$35,000
$14,240
$18,200
$25,000
$35,000
$36,000

## Slide 35: Biomass - Evenhouse
Background | Assess | Reduce | Generate | Offset | Results
Evenhouse
Notes: Using biomass energy is the same concept applied when using corn ethonol as car fuel. Biomass energy works by “growing energy as fast as you use it.”
The Even house home was a prime opportunity to explore biomass heating

## Slide 36
Background | Assess | Reduce | Generate | Offset | Results
Reeds Lake
1,250 ft2
2,000 ft2
3,000 ft2
4,000 ft2
Affholter
Boer
Cooper
DeMaagd
Evenhouse
Heffner
Koetje
Newhof
Calvin College
E Beltline
Notes: The Evenhouse home is further outside of the city as the other homes and is surrounded by several acres of woodlands. This gives enough land to sustainably grow and burn wood

## Slide 37: Biomass
Background | Assess | Reduce | Generate | Offset | Results
Evenhouse
http://www.woodmaster.com/woodfurnaces_4400.php
Notes: Concept: Grow Osage Orange to burn in a wood burner. Develop a wood plot which will sustainably grow wood, including a fallow plot.

## Slide 38
Background | Assess | Reduce | Generate | Offset | Results

## Slide 39
Background | Assess | Reduce | Generate | Offset | Results
$12,520

## Slide 40: Solar Heat - Heffner
Background | Assess | Reduce | Generate | Offset | Results
57 Therms / year-panel
http://genesisenergysolutions.com/energy-solutions/solar-thermal
http://www.climatetechwiki.org/technology/solar-heating
Heffner
Notes: Using biomass energy is the same concept applied when using corn ethonol as car fuel. Biomass energy works by “growing energy as fast as you use it.”
The Even house home was a prime opportunity to explore biomass heating

## Slide 41
Background | Assess | Reduce | Generate | Offset | Results

## Slide 42
Background | Assess | Reduce | Generate | Offset | Results
$6,300

## Slide 43: Solar PV
Background | Assess | Reduce | Generate | Offset | Results
DeMaagd
Notes: Solar Panels

## Slide 44
Background | Assess | Reduce | Generate | Offset | Results

## Slide 45
Background | Assess | Reduce | Generate | Offset | Results
$26,840

## Slide 46
Background | Assess | Reduce | Generate | Offset | Results
$37,200
$94,780
$32,190
$26,840
$32,200
$28,310
$12,000

## Slide 47
Background | Assess | Reduce | Generate | Offset | Results
Notes: Remove all homes which have achieved net zero

## Slide 48: Wind
Background | Assess | Reduce | Generate | Offset | Results
http://cleantechnica.com/2014/04/21/real-innovation-wind-energy/
http://windturbineshome.net/
Newhof

## Slide 49
Background | Assess | Reduce | Generate | Offset | Results
Cost GRAPH
http://www.calvin.edu/academic/engineering/Renewable_Energy_org/project/turbine.html

## Slide 50
Background | Assess | Reduce | Generate | Offset | Results
Notes: Remove all homes which have achieved net zero

## Slide 51
Background | Assess | Reduce | Generate | Offset | Results
$34,000

## Slide 52
Background | Assess | Reduce | Generate | Offset | Results

## Slide 53: Offset
Background | Assess | Reduce | Generate | Offset | Results
www.better-world-energy.com
Cooper
DeMaagd
Notes: Options:
Buy credits
Exchange energy
-Both produce enough to exchange energy

## Slide 54
Background | Assess | Reduce | Generate | Offset | Results

## Slide 55
Background | Assess | Reduce | Generate | Offset | Results

## Slide 56: What did we learn?
Background | Assess | Reduce | Generate | Offset | Results
Notes: All points are going to spoken. No Slides needed.
What worked?
- Solar panels are a great way to generate electricity. The payback period for grid-connected panels is now less than the life of the panels, which makes them viable.
- Reducing electricity and gas usage can be done. Especially electricity.
What didn’t work?
- Wind power is not a viable option in GR due to low wind speeds and regulations against height of wind turbines.
What unique / unexpected challenge did you face?
- A lack of environmental resources (space).
  - Roof space
  - Yard space for geothermal
- Sunlight is inconsistent in snowy climates, no reliable PV generation in the winter.
  Need bakcup electrical with Solar water heaters.
What’re the main takeaways from the project?
- Becoming net zero is very expensive today.
- A mixture of generation and reduction technologies is required.
- Reducing energy use can be done relatively inexpensive. Esp. Efficient lighting
- Insulation is more expensive, but pays back quickly and significantly reduces natural gas use.
Other comments / insights?
- Using solar and wind for energy production is intermittent. Grid connection is essential.
- Eliminating natural gas usage is a costly process with a long payback period due to the low price of natural gas today.
- Getting to net-zero has slightly less than 30-yr simple payback.

## Slide 57: What Worked?
Background | Assess | Reduce | Generate | Offset | Results
http://inhabitat.com/new-bio-solar-panels-are-made-with-cotton-and-castor-beans/
Notes: All points are going to spoken. No Slides needed.
What worked?
- Solar panels are a great way to generate electricity. The payback period for grid-connected panels is now less than the life of the panels, which makes them viable.
- Reducing electricity and gas usage can be done. Especially electricity.
What didn’t work?
- Wind power is not a viable option in GR due to low wind speeds and regulations against height of wind turbines.
What unique / unexpected challenge did you face?
- A lack of environmental resources (space).
  - Roof space
  - Yard space for geothermal
- Sunlight is inconsistent in snowy climates, no reliable PV generation in the winter.
  Need bakcup electrical with Solar water heaters.
What’re the main takeaways from the project?
- Becoming net zero is very expensive today.
- A mixture of generation and reduction technologies is required.
- Reducing energy use can be done relatively inexpensive. Esp. Efficient lighting
- Insulation is more expensive, but pays back quickly and significantly reduces natural gas use.
Other comments / insights?
- Using solar and wind for energy production is intermittent. Grid connection is essential.
- Eliminating natural gas usage is a costly process with a long payback period due to the low price of natural gas today.
- Getting to net-zero has slightly less than 30-yr simple payback.

## Slide 58: What Did Not Work?
Background | Assess | Reduce | Generate | Offset | Results
http://inhabitat.com/bladeless-wind-turbine-design-is-for-the-birds-literally/
Notes: All points are going to spoken. No Slides needed.
What worked?
- Solar panels are a great way to generate electricity. The payback period for grid-connected panels is now less than the life of the panels, which makes them viable.
- Reducing electricity and gas usage can be done. Especially electricity.
What didn’t work?
- Wind power is not a viable option in GR due to low wind speeds and regulations against height of wind turbines.
What unique / unexpected challenge did you face?
- A lack of environmental resources (space).
  - Roof space
  - Yard space for geothermal
- Sunlight is inconsistent in snowy climates, no reliable PV generation in the winter.
  Need bakcup electrical with Solar water heaters.
What’re the main takeaways from the project?
- Becoming net zero is very expensive today.
- A mixture of generation and reduction technologies is required.
- Reducing energy use can be done relatively inexpensive. Esp. Efficient lighting
- Insulation is more expensive, but pays back quickly and significantly reduces natural gas use.
Other comments / insights?
- Using solar and wind for energy production is intermittent. Grid connection is essential.
- Eliminating natural gas usage is a costly process with a long payback period due to the low price of natural gas today.
- Getting to net-zero has slightly less than 30-yr simple payback.

## Slide 59: Challenges
Background | Assess | Reduce | Generate | Offset | Results
http://news.nationalgeographic.com/news/energy/2012/02/pictures/120228-spain-solar-energy/
http://www.brainright.com/ourhouse/Construction/SolarElectric/
Notes: All points are going to spoken. No Slides needed.
What worked?
- Solar panels are a great way to generate electricity. The payback period for grid-connected panels is now less than the life of the panels, which makes them viable.
- Reducing electricity and gas usage can be done. Especially electricity.
What didn’t work?
- Wind power is not a viable option in GR due to low wind speeds and regulations against height of wind turbines.
What unique / unexpected challenge did you face?
- A lack of environmental resources (space).
  - Roof space
  - Yard space for geothermal
- Sunlight is inconsistent in snowy climates, no reliable PV generation in the winter.
  Need bakcup electrical with Solar water heaters.
What’re the main takeaways from the project?
- Becoming net zero is very expensive today.
- A mixture of generation and reduction technologies is required.
- Reducing energy use can be done relatively inexpensive. Esp. Efficient lighting
- Insulation is more expensive, but pays back quickly and significantly reduces natural gas use.
Other comments / insights?
- Using solar and wind for energy production is intermittent. Grid connection is essential.
- Eliminating natural gas usage is a costly process with a long payback period due to the low price of natural gas today.
- Getting to net-zero has slightly less than 30-yr simple payback.

## Slide 60: Challenges
Background | Assess | Reduce | Generate | Offset | Results
http://www.mercuryrefrigeration.ca/index.php?page=geothermal
Notes: All points are going to spoken. No Slides needed.
What worked?
- Solar panels are a great way to generate electricity. The payback period for grid-connected panels is now less than the life of the panels, which makes them viable.
- Reducing electricity and gas usage can be done. Especially electricity.
What didn’t work?
- Wind power is not a viable option in GR due to low wind speeds and regulations against height of wind turbines.
What unique / unexpected challenge did you face?
- A lack of environmental resources (space).
  - Roof space
  - Yard space for geothermal
- Sunlight is inconsistent in snowy climates, no reliable PV generation in the winter.
  Need bakcup electrical with Solar water heaters.
What’re the main takeaways from the project?
- Becoming net zero is very expensive today.
- A mixture of generation and reduction technologies is required.
- Reducing energy use can be done relatively inexpensive. Esp. Efficient lighting
- Insulation is more expensive, but pays back quickly and significantly reduces natural gas use.
Other comments / insights?
- Using solar and wind for energy production is intermittent. Grid connection is essential.
- Eliminating natural gas usage is a costly process with a long payback period due to the low price of natural gas today.
- Getting to net-zero has slightly less than 30-yr simple payback.

## Slide 61: Takeaways
Background | Assess | Reduce | Generate | Offset | Results
http://10-most.com/the-top-ten-most-expensive-things-in-the-world/
Notes: All points are going to spoken. No Slides needed.
What worked?
- Solar panels are a great way to generate electricity. The payback period for grid-connected panels is now less than the life of the panels, which makes them viable.
- Reducing electricity and gas usage can be done. Especially electricity.
What didn’t work?
- Wind power is not a viable option in GR due to low wind speeds and regulations against height of wind turbines.
What unique / unexpected challenge did you face?
- A lack of environmental resources (space).
  - Roof space
  - Yard space for geothermal
- Sunlight is inconsistent in snowy climates, no reliable PV generation in the winter.
  Need bakcup electrical with Solar water heaters.
What’re the main takeaways from the project?
- Becoming net zero is very expensive today.
- A mixture of generation and reduction technologies is required.
- Reducing energy use can be done relatively inexpensive. Esp. Efficient lighting
- Insulation is more expensive, but pays back quickly and significantly reduces natural gas use.
Other comments / insights?
- Using solar and wind for energy production is intermittent. Grid connection is essential.
- Eliminating natural gas usage is a costly process with a long payback period due to the low price of natural gas today.
- Getting to net-zero has slightly less than 30-yr simple payback.

## Slide 62: Take Home Message
Background | Assess | Reduce | Generate | Offset | Results
http://superfastlinkbuilding.com/wp-content/uploads/2012/04/How-Green-Affiliate-Marketing-Can-Grow-Your-Sustainable-Business-1.jpg
Take small steps toward energy efficiency
Notes: Space Confinement issues
Horizontal Loop is inexpensive if home has the space

## Slide 63: Take Home Message
Background | Assess | Reduce | Generate | Offset | Results
http://assets.inhabitat.com/wp-content/blogs.dir/1/files/2011/08/Zimbabwe-CLF-bulb-exchange-3-537x402.jpg
Notes: Space Confinement issues
Horizontal Loop is inexpensive if home has the space

## Slide 64: Take Home Message
Background | Assess | Reduce | Generate | Offset | Results
Chart: Payback Period - LED Bulbs
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
LED Bulbs | -957 | -257.88 | 441.24 | 1140.36 | 1839.48 | 2538.6 | 3237.72 | 3936.84 | 4635.96 | 5335.08 | 6034.2 | 6733.32 | 7432.44 | 8131.56 | 8830.68 | 9529.8 | 10228.92 | 10928.04 | 11627.16 | 12326.28 | 13025.4
Cooper
Notes: Space Confinement issues
Horizontal Loop is inexpensive if home has the space

## Slide 65: Take Home Message
Background | Assess | Reduce | Generate | Offset | Results
http://www.ci.bellaire.tx.us/index.aspx?NID=917
Notes: Make sure your home is properly insulated

## Slide 66: Take Home Message
Background | Assess | Reduce | Generate | Offset | Results
http://www.realestate.com.au/blog/a-household-history-of-the-fridge-2/
http://www.geappliances.com/appliances/refrigerators/cafe-hot-water-french-door-refrigerator/
Notes: Make sure your home is properly insulated

## Slide 67
Background | Assess | Reduce | Generate | Offset | Results
Notes: Make sure your home is properly insulated

## Slide 68: Take Home Message
http://2.bp.blogspot.com/-WQcK_tUJq2M/UR49huX812I/AAAAAAAAFoo/oDNyAeYhV5A/s1600/Sustainable-Home.png
“The choice you make that will have the biggest impact on your environmental footprint is what kind of house you live in.”
- Professor Heun
Background | Assess | Reduce | Generate | Offset | Results
Notes: Make sure your home is properly insulated

## Slide 69: Net-Zero House Study
Engineering 333 Class Project
Senior Mechanical Engineering Students
12/02/2014

## Slide 70: Compiled Technology Payback
Chart: Low to High Payback Period
| Lifestyle | LED Bulbs | Oven (electric) | Dryer | Biomass (wood stove) | Kitchen Appliances | Insulation | Water Heater | Fridge | Solar Absorbers | Washing Machine | Freezer | Solar | Geothermal | Wind | Windows | Stove | Oven (gas)
 | 0 | 1.96 | 3.42 | 5.35 | 5 | 5.88 | 12.05 | 16.28 | 21.25 | 23.94 | 25.06 | 28.74 | 30.38 | 31.05 | 40.48 | 45.73 | 49.39 | 146.14

## Slide 71: Compiled Technology Payback
Chart: High to Low Investment Cost
| Solar | Wind | Geothermal | Biomass (wood stove) | Solar Absorbers | Windows | Insulation | Water Heater | Stove | Fridge | Washing Machine | Oven (gas) | LED Bulbs | Dryer | Kitchen Appliances | Freezer | Lifestyle
 | 30.38 | 40.48 | 40.99 | 5 | 23.94 | 45.73 | 12.05 | 16.28 | 49.39 | 21.25 | 25.06 | 146.14 | 1.96 | 5.35 | 5.88 | 28.74 | 0

## Slide 72: Payback Period – Electricity
Chart: Technology
| Lifestyle | LED Bulbs | Oven | Dryer | Kitchen Appliances | Fridge | Washing Machine | Freezer | Solar | Wind
 | 0 | 1.96 | 3.42 | 5.35 | 5.88 | 21.25 | 25.06 | 28.74 | 30.38 | 40.48

## Slide 73: Payback Period – Gas
Chart: Technology
| Biomass (wood stove) | Insulation | Water Heater | Dryer | Solar Absorbers | Geothermal | Windows | Stove | Oven
 | 5 | 12.05 | 16.28 | 16.48 | 23.94 | 40.99 | 45.73 | 49.3859 | 146.14

## Slide 74: Payback Period – Renewable Energy
Chart: Payback Period - Renewable Energy
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45
Geothermal | -21845.4 | -21141.8062 | -20438.2124 | -19734.6186 | -19031.0248 | -18327.431 | -17623.8372 | -16920.2434 | -16216.6496 | -15513.0558 | -14809.462 | -14105.8682 | -13402.2744 | -12698.6806 | -11995.0868 | -11291.493 | -10587.8992 | -9884.3054 | -9180.7116 | -8477.1178 | -7773.524 | -7069.9302 | -6366.3364 | -5662.7426 | -4959.1488 | -4255.555 | -3551.9612 | -2848.3674 | -2144.7736 | -1441.1798 | -737.586 | -33.9922 | 669.6016 | 1373.1954 | 2076.7892 | 2780.383 | 3483.9768 | 4187.5706 | 4891.1644 | 5594.7582 | 6298.352 | 7001.9458 | 7705.5396 | 8409.1334 | 9112.7272 | 9816.321
Solar Absorber | -6300 | -6036.8826 | -5773.7652 | -5510.6478 | -5247.5304 | -4984.413 | -4721.2956 | -4458.1782 | -4195.0608 | -3931.9434 | -3668.826 | -3405.7086 | -3142.5912 | -2879.4738 | -2616.3564 | -2353.239 | -2090.1216 | -1827.0042 | -1563.8868 | -1300.7694 | -1037.652 | -774.5346 | -511.4172 | -248.2998 | 14.8176 | 277.935 | 541.0524 | 804.1698 | 1067.2872 | 1330.4046 | 1593.522 | 1856.6394 | 2119.7568 | 2382.8742 | 2645.9916 | 2909.109 | 3172.2264 | 3435.3438 | 3698.4612 | 3961.5786 | 4224.696 | 4487.8134 | 4750.9308 | 5014.0482 | 5277.1656 | 5540.283
Wind | -34000 | -33160 | -32320 | -31480 | -30640 | -29800 | -28960 | -28120 | -27280 | -26440 | -25600 | -24760 | -23920 | -23080 | -22240 | -21400 | -20560 | -19720 | -18880 | -18040 | -17200 | -16360 | -15520 | -14680 | -13840 | -13000 | -12160 | -11320 | -10480 | -9640 | -8800 | -7960 | -7120 | -6280 | -5440 | -4600 | -3760 | -2920 | -2080 | -1240 | -400 | 440 | 1280 | 2120 | 2960 | 3800
Solar Panel | -44640.2 | -43170.584 | -41700.968 | -40231.352 | -38761.736 | -37292.12 | -35822.504 | -34352.888 | -32883.272 | -31413.656 | -29944.04 | -28474.424 | -27004.808 | -25535.192 | -24065.576 | -22595.96 | -21126.344 | -19656.728 | -18187.112 | -16717.496 | -15247.88 | -13778.264 | -12308.648 | -10839.032 | -9369.416 | -7899.8 | -6430.184 | -4960.568 | -3490.952 | -2021.336 | -551.72 | 917.896 | 2387.512 | 3857.128 | 5326.744 | 6796.36 | 8265.976 | 9735.592 | 11205.208 | 12674.824 | 14144.44 | 15614.056 | 17083.672 | 18553.288 | 20022.904 | 21492.52

## Slide 75: Payback Period – Renewable Energy